## Slide 1: LCD Display
Lab 05

## Slide 2: Your Task
Display characters according to the button pressed
A
B
C
…
ABC_

## Slide 3: Grading
Basic: (60%)
  Display the character pressed at the cursor position
Bonus 1: (+10%)
  Implement the `new-line’ key
  Change to the next line if new-line pressed at Line 1
  Scroll the screen if new-line pressed at Line 2
Bonus 2: (+20%)
  Implement the arrow keys (up, down, left, right)
  Move the cursor by the arrow key
  Insert character at the cursor position

## Slide 4: Control the LCD Display
From the hardware perspective

## Slide 5: Signal Interface to the LCD
The application processor sends commands and data through port P3
A command:
  Moving cursor
  Clear screen
  …etc
Data: the ASCII code of the character to display

## Slide 6: Signal interface to the LCD
RS: register select
  0: command
  1: data
E: latch enable
  the LCD latches the command/data at negative edge (10)
D [7:0]
  the 8-bit data/command
  configured 4-bit mode
  send higher portion first

## Slide 7: List of commands
http://www.eeherald.com/section/design-guide/sample_lcd_c_programs.html

## Slide 8: Timing diagram to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
latch data
Higher-half of
the data
Lower-half of
the data
latch data

## Slide 9: Timing diagram to send command/data
Example: to send command 0x01
clear screen, cursor home
E
RS
D[3:0]
0
0
0
1
time
latch command
Higher-half of
the command
Lower-half of
the command
latch command

## Slide 10: How to program the LCD
Demo: LCD_Hello

## Slide 11: Initialize the LCD

## Slide 12: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
latch data
Higher-half of
the data
Lower-half of
the data
latch data
Prepare the status word

## Slide 13: Program to send command/data
Example: to send data ‘A’=0x41
The LCD prints ‘A’ at the cursor position
E
RS
D[3:0]
1
4
1
1
time
latch data
Higher-half of
the data
Lower-half of
the data
latch data
Send out from port P3

## Slide 14: Your Mid-Term Project

## Slide 15: Project: Count-Down Bomb
setup count-down timer by buttons
display residual time on the LCD
input password from buttons to stop count-down
explode the bomb when (1) time up (2) press the wrong password
A
B
C
D

## Slide 16: Grading
Basic: count-down timer (60%)
  display time mm:ss and refresh every second
  count-down from 59:59
Additional function at setup stage:
  setup the timer by buttons (5%)
  blink the cursor on the digit to be set when you are setting up the time: 10%
Additional function at count-down stage:
  speed-up counting when someone is trying to input the password (10%)
    refresh every 0.1 second
  make all digits blink when time-up/wrong password: 10%
Still bonus for additional functions you defined
your report: 10%

## Slide 17: Mid-Term Project Proposal
The algorithm framework of your alarm/stop-watch
Key Issue: your time-sharing scheme for multiple events and hardware devices
  LCD display
  button input
  timer events